Ohm's Law

For many types of circuit elements, there exists a simple relationship between voltage applied to the element, and the resulting charge flow, or current. In this portion of the experiment we will investigate the relationship between voltage and current for a wire-wound resistor. In Electronics, use is made of simplified drawings known as "schematics" These schematics are designed to show the electrical connections made between the varying circuit elements. (A complete list of the symbols used when drawing schematics can be found in the back of your text). Following the schematic, draw the connections to this circuit below (Figure 2-2) (Use a pencil when making your drawing below - you may need to correct it!)

| Introduction to Electronics Lab | EET103- | SECTION: | Exp #2: "Ohm's Law" | Page 1/5 |
| --- | --- | --- | --- | --- |

| Name: | Date: |  |
| --- | --- | --- |

Since we do not have the power supply we will connect our 9V battery in its place and our rheostat will be a bit different, but I have numbered the pins the same as before. It is a round unit , also we will use a 1500 Ohm resistor . Connect your circuit asn set the rheostat to middle range of its turn radius and place your multimeter in series in the circuit to measure the current. Touch to the battery and get a current reading. Then take out the mutimeter and replace it with a clip lead. Switch yur voltameter over to read voltage and connect it to both sides of the resistor. Again quickly touch the power to the circuit and take a voltage rading. This action is necessary since we only have one meter at home. But, as it is a multimeter, we can do both operations. [You should see about 1 to 2 mA and about 3 V.) Record your readings below: Using Ohm's Law, R1's value can now be calculated: Now, disconnect the power supply - and temporarily remove R1 from the circuit. Be careful! R1 may be hot! Using the DIGITAL VOM, measure the Actual value of R1 (The value of R1 determined above using Ohm's law - and the "actual" measured value should be close - within 10%)

| Page 2/5 | Introduction to Electronics Lab | Experiment #2 "Ohm's Law" |
| --- | --- | --- |

Part-2 As we increase or decrease the charge flowing into a resistor, the VOLTAGE across that resistor will change also. This relationship should be governed by Ohm's Law. To demonstrate this, we will leave the supply voltage (VT) at a constant 9 volts. (not much choice since it is a battery.) We will then incrementally increase the flow of charge (current) through the 1500 fixed resistor R1 - by adjusting the Rheostat R2 We will observe the current flowing through R1 - While also noting the Voltage drop across R1 Reconnect R1 in the circuit. Carefully move the wiper on the Rheostat to obtain a current as close to 1 mA as you can. Record the resulting current and voltages Voltages across R1 below as yu change the rheostat. Use your data from above, to complete the graph below. . .

| Introduction to Electronics Lab | Experiment #2 "Ohm's Law" | Page 3/5 |
| --- | --- | --- |

Recall from Algebra class, that the equation of a straight line is: y = mx + b where . . . y = Vertical axis value x = Horizontal value b = Intercept on y axis at x = 0 m = Slope of the line To measure the slope of a line once the quantities are measured, start by picking two points on the graph. (see below) The is read as "change in". Another definition of slope is "rise over run" This refers to the length of the sides of the triangle as seen below in Figure 2-4 Using your voltage-current curve from page-3, determine the Slope. (Compare your SLOPE to the "Ohm's Law" value of R1 - They should be the same)

| Page 4/5 | Introduction to Electronics Lab | Experiment #2 "Ohm's Law" |
| --- | --- | --- |

Electrical devices which have linear (straight-line) relations between voltage and current are called "Ohmic" It is possible for electrical devices to be "Non-Ohmic" and electrical circuits make use of both kinds. Shown below are some types of "Non-Ohmic" devices. . . _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________

| Introduction to Electronics Lab | Experiment #2 "Ohm's Law" | Page 5/5 |
| --- | --- | --- |

Rev.1L  T.CARROLL  7-4-97  This document is archived on the KEPLER Network filename:  F:\SHARABLE\HANDOUTS\EET103\lab02.doc  (MS Word 2.0)