| Case-3 Four Parallel Resistors Calculate the Total resistance from the circuit above. Using Figure 3-4, draw the circuit connections, then wire the circuit. Using both the DMM and VOM, measure the circuits total resistance. |
| --- |
| Page 4/7 | Introduction to Electronics Lab | Exp #3 "Series/Parallel Resistor Combinations" |
| Case-4 Series / Parallel Circuit Calculate the Total resistance from the circuit above. Using Figure 3-5, draw the circuit connections, then wire the circuit. Using both the DMM and VOM, measure the circuits total resistance. |
| Introduction to Electronics Lab | Exp #3 "Series/Parallel Resistor Combinations" | Page 5/7 |
| Case-5 Combination Circuit Calculate the Total resistance from the circuit above. Using Figure 3-4, draw the circuit connections, then wire the circuit. Using both the DMM and VOM, measure the circuits total resistance. |
| Page 6/7 | Introduction to Electronics Lab | Exp #3 "Series/Parallel Resistor Combinations" |
| _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ |
| Introduction to Electronics Lab | Exp #3 "Series/Parallel Resistor Combinations" | Page 7/7 |

Rev.1C  T.CARROLL  7-15-97  This document is archived on the KEPLER Network filename:  F:\SHARABLE\HANDOUTS\EET103\lab03_2.doc  (MS Word 2.0)