| 741 Linear Operational Amplifier Computer Simulation Experiment by MultiSim |
| --- |
| The Linear Operational Amplifier (Op-Amp) is supposed to give an output voltage that is a multiple of the input signal. There are two circuit configuration for Op-Amp: Non-Inverted Op-Amp (noninv.ms10) Inverted Op-Amp (invert.ms10) PART I: Non-Inverted Op-Amp Vout = Av * Vin Av = (1 + Rf / Ri) (Non-Inverting Op-Amp: Calculated Voltage Gain Formula) Av = Vout / Vin (Measured Voltage Gain Formula) where: Av - the gain of the amplifier Rf - Feedback Resistance Ri - Input Resistance NON-INVERTED AMPLIFIER CIRCUIT CONFIGURATION |
| Introduction to Electronics Lab | EET103- | SECTION: | Experiment: "The Op-Amp" |  |
| Name: | Date: | Page 1/5 |
| Using the diagram above, construct the circuit above or down load from the website. Using the Oscilloscope, set the frequency of the function generator to 1KHz at a voltage of 100mV peak to peak. Apply this signal to the positive input (Non-Inverting Input) of your amplifier and measure the output: Now determine the Measured Voltage Gain of the Non-Inverting Amplifier and record in the Table below: Also, Calculate The Voltage Gain of the Non-Inverting Amplifier and Record in the Table below: How close are the Measured and Calculated voltage Gain? Replace the 10K resistor with a 47 k and 100K and repeat the measurements: Rf (Feedback R) Vin Vout Av(Meas.) = Vout/Vin Av(Cal.) = (1 + Rf / Ri) Av (dB) = 20 log Av Rf = 10kΩ ? ? ? ? ? Rf = 47 kΩ ? ? ? ? ? Rf = 100 kΩ ? ? ? ? ? |
| Page 2/5 | Introduction to Electronics Lab |  |
| Increase the amplitude of the input signal until the output signal begins to "flatten" out on top, or the signal is "clipped" Measure the positive and negative maxims at which this occurs. (They will be close in value but need not be of equal magnitude) Record these measured valus in Table below: Vin = ? Vout (pos. peak) = ? Vout (neg. peak) = ? How do these values compare to the 12V available from the power supply? __________________________________________________________________________________________________________________________________________________________________________________________________________________________ __________________________________________________________________________________________________________________________________________________________________________________________________________________________ __________________________________________________________________________________________________________________________________________________________________________________________________________________________ __________________________________________________________________________________________________________________________________________________________________________________________________________________________ PART II: Inverted Op-Amp Vout = Av * Vin Av = - Rf / Ri (Inverting Op-Amp: Calculated Voltage Gain Formula) Av = Vout / Vin (Measured Voltage Gain Formula) where: Av - the gain of the amplifier Rf - Feedback Resistance Ri - Input Resistance INVERTED AMPLIFIER CIRCUIT CONFIGURATION |
| Introduction to Electronics Lab |  | Page 3/5 |
| Using the diagram above, construct the circuit above or down load from the website. Using the Oscilloscope, set the frequency of the function generator to 1KHz at a voltage of 100mV peak to peak. Apply this signal to the negative input (Inverting Input) of your amplifier and measure the output: Now determine the Measured Voltage Gain of the Inverting Amplifier and record in the Table below: Also, Calculate The Voltage Gain of the Inverting Amplifier and Record in the Table below: How close are the Measured and Calculated voltage Gain? Replace the 10K resistor with a 47 k and 100K and repeat the measurements: Rf (Feedback R) Vin Vout Av(Meas.) = Vout/Vin Av(Cal.) = - Rf/Ri Av (dB) = 20 log Av Rf = 10kΩ ? ? ? ? ? Rf = 47 kΩ ? ? ? ? ? Rf = 100 kΩ ? ? ? ? ? |
| Page 4/5 | Introduction to Electronics Lab |  |
| Increase the amplitude of the input signal until the output signal begins to "flatten" out on top, or the signal is "clipped" Measure the positive and negative maxims at which this occurs. (They will be close in value but need not be of equal magnitude) Record these measured valus in Table below: Vin = ? Vout (pos. peak) = ? Vout (neg. peak) = ? How do these values compare to the 12V available from the power supply? __________________________________________________________________________________________________________________________________________________________________________________________________________________________ __________________________________________________________________________________________________________________________________________________________________________________________________________________________ __________________________________________________________________________________________________________________________________________________________________________________________________________________________ __________________________________________________________________________________________________________________________________________________________________________________________________________________________ OBSERVATIONS/CONCLUSIONS: _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ _________________________________________________________________________________________________________________________________ |
| Introduction to Electronics Lab |  | Page 5/5 |