Lesson 8: Operational Amplifier – Problem Set

- An op amp is wired as a non-inverting circuit with R1= 1K and R2= 4.7 K.  What is the circuit diagram and the gain?

- A 741 op amp is used in the above.  Label the PIN OUTs of the amp to match a DIP package.

- An inverting op amp has a gain of 100 and needs an input impedance of 1.5 KW.  What will the R1 and R2 values need to be?

- Draw an inverting adder circuit to add two input voltages of 0.2 V and 0.35 V and produce an output of 7 V.

- The circuit below is a 9V battery tester.  If the applied voltage is less that 7.5 V, the red LED should glow. If above 7.5 V the green LED will glow.  Select values for R1 and R2 that will allow this to happen and label the LEDs as red and green.